## Slide 1: Fall Detection using 24 Ghz MM wave radar sensor
Akash Jena

## Slide 2: Project Overview
Objective: Detect and classify human activities (Sitting, Standing, Walking, Falling) to identify fall-prone behaviors using radar data.
Hardware Used:
  Seeed Studio 24GHz mmWave Sensor (MR24D11C10): Detects movement and presence.
  XIAO BLE Sense Board: Microcontroller used to read sensor data.
  SD Card Module: Used to log raw radar data for training.
Approach:
  Use raw byte data from the radar sensor.
  Train a 1D CNN model to classify activities based on those bytes.

## Slide 3: Setup

## Slide 4: Data Collection
Sensor Output Details:
  Each radar frame outputs bytes representing various features.
  Bytes at index 4 (Presence byte) and 8 (energy signal byte) selected for training (2 features per timestep).
Arduino Logging:
  Radar bytes collected and logged to SD card via serial interface.
Sampling:
  300 samples per class initially collected (Sitting, Standing, Walking).
  Each sample consists of a fixed number of timesteps.

## Slide 5: Preprocessing Steps
Hex to Int Conversion:
  Raw bytes are in hexadecimal format and converted to integers.
Activity Labeling:
  Sitting: Label 0
  Standing: Label 1
  Walking: Label 2
Reshape for CNN:
  Final shape: (samples, timesteps, 2 features)
Normalization:
  All features normalized to ensure stable training.

## Slide 6: Model Architecture
Model Type: 1D Convolutional Neural Network (CNN)
Layer Breakdown:
  Conv1D Layer: Captures temporal features across byte sequences.
  MaxPooling1D: Reduces dimensionality and computation.
  Flatten Layer: Converts output to 1D vector.
  Dense (ReLU): Learns complex patterns.
  Output Dense (Softmax): Predicts class probabilities.
Training Setup:
  Loss Function: Categorical Crossentropy
  Optimizer: Adam
  Accuracy Metric Used

## Slide 7: Experiment 1 - Imbalanced Data
Class Distribution:
  Sitting: 120 samples
  Standing: 120 samples
  Walking: 300 samples
Split: 80% Training, 20% Testing
Results:
  Achieved 98% accuracy on test set
Analysis:
  Model biased towards walking due to class imbalance
  Overfitting likely due to small sample size for Sitting/Standing

## Slide 8: Experiment 2 - Balanced Data
Balanced Class Distribution:
  300 samples each for Sitting, Standing, and Walking
Split: 80% Training, 20% Testing
Results:
  Accuracy dropped to 85%
Analysis:
  Better data balance but poor generalization
  Model may need more data or tuning

## Slide 9: Analysis and Next Steps
Key Takeaways:
  Balanced data gives realistic accuracy.
  Accuracy drop indicates model needs improvement.
Problems Identified:
  Limited training samples (only 300/class)
  Radar bytes used might not be optimal features.
Next Steps:
  Collect 1000 samples/class
  Divide each class into: 800 training, 100 validation, 100 testing
  Tune model using validation data
  Try alternate models (LSTM, 2D CNN)
  Apply data smoothing or filtering techniques

## Slide 10: Conclusion
Achievements:
  Successfully implemented basic activity classification using radar and 1D CNN
Challenges:
  Accuracy varies significantly with dataset balance
Planned Improvements:
  Expand dataset for robustness
  Experiment with different byte selections and models
  Apply validation techniques for better generalization

## Slide 11
THANK YOU